## Slide 1
Lecture # 3:
WAN
Data Communication Network

## Slide 2: Outline
Data Communication Network Taxonomy
  Broadcast vs. Switched Networks
  Circuit Switched vs. packet switched
Switched Network Performance
  Delay, Lose, Throughtput

## Slide 3: Network Taxonomy
Data Communication Networks
Switched networks
Broadcast networks

## Slide 4: 1. Broadcast networks
  Nodes share a common channel; information transmitted by a node is received by all other nodes in the network.
  Broadcast Network (used in LAN)
  Examples: TV, radio

## Slide 5: 2. Switching Networks
Long distance transmission is typically done over a network of switched nodes
End devices are referred to as stations
  Computer, terminal, phone, etc.
A collection of nodes and connections is a communications network
Data is routed by being switched from node to node
  Information is transmitted to a small sub-set (usually only one) of the nodes

## Slide 6: 2. Switching Networks cont…
Communication Network
  Switching Network (used in WAN)
Switching Networks
  Circuit-switching networks
  Packet-switching networks

## Slide 7: 2. Switched Network cont…
Switched
networks
Circuit-switched
networks
FDM
TDM
Packet-switched
networks
Networks
with VCs
Datagram
Networks
(Internet)
(X.25,Frame relay, ATM)
Course Subject

## Slide 8: 2.1 Circuit Switching
Circuit switching is a technique that directly connects the sender and the receiver in an unbroken path.
Telephone switching equipment, for example, establishes a path that connects the caller's telephone to the receiver's telephone by making a physical connection.

## Slide 9: 2.1 Circuit Switching cont…
With this type of switching technique, once a connection is established, a dedicated path exists between both ends until the connection is terminated.
Routing decisions must be made when the circuit is first established, but there are no decisions made after that time.

## Slide 10
circuit establishment
DATA
data transmission
circuit termination
propagation delay
from A to Node 1
propagation delay
from B To A
processing delay at Node 1
Circuit Switching in MultiHop Route
A
B
Node 1
Node 2

## Slide 11: 2.1 Circuit switching cont…
Advantages:
  The communication channel (once established) is dedicated.
Disadvantages:
  Possible long wait to establish a connection, (10 seconds,
  more on long- distance or international calls.) during which
  no data can be transmitted.
  More expensive than any other switching techniques,
  because a dedicated path is required for each connection.
  Inefficient use of the communication channel, because the
  channel is not used when the connected systems are not
  using it.

## Slide 12: 2.1 Circuit Switching cont…
Dividing link bandwidth into “pieces”:
  2.1.1 Frequency Division Multiplexing (FDM)
  2.1.2 Time Division Multiplexing (TDM)

## Slide 13: Circuit Switching: FDM and TDM
2.1 Frequency Division Mux (FDM)
bandwidth/
frequency
of the link
time
4 users/slots
Example:
f
t
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 14: Time Division Multiplexing (TDM)
Two or more “channels” of information are transmitted over the same link by allocating a different time interval for the transmission of each channel, i.e. the channels take turns to use the link.
TDM becomes inefficient when traffic is intermittent because the time slot is still allocated even when the channel has no data to transmit

## Slide 15: Circuit Switching: FDM and TDM cont…
2.2 Time Division Mux (TDM)
bandwidth/
frequency
of the link
time
Slot
4 slots/frame
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 16: 2.2 Time Division Mux (TDM)

## Slide 17: Packet Switching
packet switching methods, is broken into small parts, called packets.
With current technology, packets are generally accepted onto
the network on a first-come, first-served basis. If the network
becomes overloaded, packets are delayed or discarded
(``dropped'').

## Slide 18: 2.2 Packet-switched Networks: Features:
Data separated into packets
Switching decision (output port) for each individual packet
Statistical multiplexing: Sum of peak rates may exceed.

## Slide 19: Timing Diagram of Packet Switching
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
processing and queueing delay of Packet 1 at router 2
propagation
delay from
Host A to
router 1
transmission
time of Packet 1
at Host A

## Slide 20: 2.2 Packet-switched Networks: Forwarding
Goal: move packets through routers from source to dest
(1) Packet-switched datagram network:
  destination address in packet determines next hop
  Entire packet must arrive at router before it can be transmitted on next link
  routes may change during session
(2) Packet-switched virtual circuit network:
  each packet carries tag (VC ID), tag determines next hop
  fixed path determined at call setup time.

## Slide 21: Datagram
Each packet treated independently
Packets can take any practical route
Packets may arrive out of order
Packets may go missing
Up to receiver to re-order packets and recover from missing packets

## Slide 22: Virtual Circuit
In the virtual circuit approach, a route is established before any data packets are sent.
A logical connection is established when
a sender send a "call request packet" to the receiver and
the receiver send back an acknowledge packet "call accepted
packet" to the sender if the receiver agrees on conversational
parameters.
Virtual circuits imply acknowledgements, flow control, and error
control, so virtual circuits are reliable.

## Slide 23: Packet Switching : Virtual Circuit
The difference between virtual circuit and datagram approaches:
With virtual circuit, the node does not need to make a routing
decision for each packet.
It is made only once for all packets using that virtual circuit.

## Slide 24: Packet Switching: Virtual Circuit
VC's offer guarantees that
the packets sent arrive in the order sent
with no duplicates
with no errors.

## Slide 25: Packet Switching vs Circuit Switching
Great for burst data
  resource sharing
  simpler, no call setup
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem
Is packet switching a “slam dunk winner?”

## Slide 26: Switching technology
Circuit switching
  need a connection established between end nodes
  connection is maintained until one of end nodes terminates
  Connection is dedicated to the communication between two nodes
  Example : Public Switch Telephone Network (PSTN)
Packet switching
  data are transmitted in short messages called packets
  a connection between the two end-nodes is not maintained
  a node-to-node link can be dynamically shared by many packets
  Example : Public Data Network (PDN) like X.25, Frame Relay
Notes: The type of data communication facility used is a function of the nature of the application, the number of computers involved, and their physical interface.

## Slide 27: Disadvantages of packet switching
Disadvantages:
  Protocols for packet switching are typically more complex.
  It can add some initial costs in implementation.
  If packet is lost, sender needs to retransmit the data.
  Another disadvantage is that packet-switched systems still
  can’t deliver the same quality as dedicated circuits in
  applications requiring very little delay - like voice
  conversations or moving images.

## Slide 28
Delay Calculation in Circuit Switched Networks
Transmission delay:
R = reserved bandwidth (bps)
L = packet length (bits)
time to send a packet into link = L/R
Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x105 km/sec)
propagation delay = d/s
Propagation delay: delay for the first bit to go from a source to a destination
Transmission delay: time to pump data onto link at reserved rate
DATA
d/s
L/R
Time

## Slide 29: An Example
Propagation delay
  suppose the distance between A and B is 4000 km, then one-way propagation delay is:
Transmission delay
  suppose we reserve a one slot GSM channel
    a GSM frame can transmit about 115 kbps
    A GSM frame is divided into 8 slots
    each reserved one slot GSM has a bandwidth of about 14 Kbps (=115/8)
  then the transmission delay of a packet of 1 Kbits is

## Slide 30: An Example (cont.)
Suppose the setup message is very small, and the total setup processing delay is 200 ms
Then the delay to transfer a packet of 1 Kbits from A to B (from the beginning until host receives last bit of the file) is:
DATA
20 + 200
20
20
70
Host A
Host B
time

## Slide 31: Another example
How long does it take to send a file of 640,000 bits (1 byte=8bits) from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps (Mega Bits Per Second)
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit (setup time including propagation delay)
Single circuit speed = 1.536 Mbps / 24 = 64kbps
File transmission time = 500 msec + file size/speed
= 0.5 sec + 640,000 bits / 64
= 10.5 sec
Kb/s

## Slide 32: How do loss and delay occur in packet switching?
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 33: packet delay
A
B
propagation
transmission
queueing

## Slide 34
Total Delay in Datagram Networks
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
nodal processing and queueing delay of Packet 1 at Node 2
propagation
delay between
Host 1 and
Node 2
transmission
time of Packet 1
at Host 1
Host 1
Host 2
Node 1
Node 2

## Slide 35: Packet loss
queue preceding link in buffer has finite capacity
packet arriving to full queue dropped
lost packet may be retransmitted by previous node, by source end system, or not at all.
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)

## Slide 36: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver

## Slide 37
Circuit Switch vs. Packet switch
Sr #
Circuit Switch
Packet Switch
1.
Forwarding decision at the time of call arrival. Thus, no header is required
Forwarding decision every time a new packet arrives.
2
Circuit switched call lasts for few minutes
New packet may arrive every few sec
3
No buffer required
buffer required

## Slide 38: Summary
Network Taxonomy
  Broadcast
  Circuit Switch
  Packet switch
  Virtual circuit switch
Switched Network Performance
  Delay, packet loss, throughput

## Slide 39
End Slide Show # 3